## Slide 1: Solid Edge ST5 Training Sketching

## Slide 2: 3D Sketching Overview
Sketch workflow
Activity: Draw a simple sketch

## Slide 3: Locking the sketch plane
Automatic plane locking
Manual plane locking
Using the lock icon to lock or unlock a sketch plane
Using the F3 function key to lock a plane

## Slide 4: Drawing synchronous sketches
Lock to a face or plane to draw sketch
Alignment lines
Using a grid

## Slide 5: Drawing synchronous sketches
regions
Activity: Create regions

## Slide 6: Drawing synchronous sketches
open sketches

## Slide 7: Synchronous sketch behavior in the ordered environment
Synchronous sketch dimensions are not migrated to ordered features.
Synchronous sketches are not consumed when creating an ordered feature.
Synchronous sketches can drive ordered features.
Synchronous sketches appear while in the ordered environment.
Regions are disabled.
Synchronous sketches appear in the synchronous sketch style and colors.
When using the Select Tool in the ordered environment, synchronous sketch elements locate as individual elements.
Synchronous sketches can be moved using the steering wheel handle. The entire sketch moves (not single elements).
In the ordered environment, synchronous sketch geometry or relationships commands are not available.
Synchronous and ordered sketches cannot be copied while in ordered environment.
Manual plane locking
Using the lock icon to lock or unlock a sketch plane
Using the F3 function key to lock a plane

## Slide 8: Drawing ordered sketches
    Workflow
    Choose the sketch command.
    Select a reference plane or part face as the sketch plane.
    Automatically enter the sketch environment.
    Draw sketch elements.
    Add sketch geometric relationships and functional variables.
    Add sketch dimensions.
    Close the sketch environment.

## Slide 9: Drawing 2D elements
    Overview
    Intent zones
    Construction geometry
    Modifying sketch elements
    Applying colors and patterns to closed sketch boundaries

## Slide 10: Geometric relationships
    The sketch relationship commands are located on the Sketching tab (1) in the Relate group (2).
    Note: When creating a synchronous feature, the sketch relationships do not migrate to the feature created from them.
    Relationships

## Slide 11: Drawing tools
    Working with grids
    IntelliSketch
    Projection lines
    Distance and area measurements in sketches

## Slide 12: Dimensioning sketches
    Dimensioning commands are located in three locations. They are located in the Dimension group on the Home, Sketching and PMI tabs.
    Locked dimensions
    Dimension orientation
    Dimension style

## Slide 13: Sketches in PathFinder
    Sketches context menu in PathFinder
    Used Sketches context menu in PathFinder

## Slide 14: Sketch consumption and dimension migration
    Working with combinable sketches

## Slide 15: Manipulating sketches
    Moving and copying sketches
    Projecting elements to a sketch

## Slide 16: Sketching activities
    (3) Instructional activities
    (5) Creating a sketch from a dimensioned drawing